## Slide 1: Digital Integrated Circuits A Design Perspective
Introduction
Jan M. Rabaey
Anantha Chandrakasan
Borivoje Nikolic

## Slide 2: What is this book all about?
Introduction to digital integrated circuits.
  CMOS devices and manufacturing technology. CMOS inverters and gates. Propagation delay, noise margins, and power dissipation. Sequential circuits. Arithmetic, interconnect, and memories. Programmable logic arrays. Design methodologies.
What will you learn?
  Understanding, designing, and optimizing digital circuits with respect to different quality metrics: cost, speed, power dissipation, and reliability

## Slide 3: The First Computer

## Slide 4: ENIAC - The first electronic computer (1946)

## Slide 5: The Transistor Revolution
First transistor
Bell Labs, 1948

## Slide 6: The First Integrated Circuits
Bipolar logic
1960’s
ECL 3-input Gate
Motorola 1966

## Slide 7: Moore’s Law
In 1965, Gordon Moore noted that the number of transistors on a chip doubled every 18 to 24 months.
He made a prediction that semiconductor technology will double its effectiveness every 18 months

## Slide 8: Moore’s Law
Electronics, April 19, 1965.

## Slide 9: LMC Metric (Logic)

## Slide 10: LMC Metric (Memory)

## Slide 11: LMC Metric (Interconnect)

## Slide 12: Design Abstraction Levels
n+
n+
S
G
D
+
DEVICE
CIRCUIT
GATE
MODULE
SYSTEM

## Slide 13: Design Metrics
How to evaluate performance of a digital circuit (gate, block, …)?
  Cost
  Reliability
  Scalability
  Speed (delay, operating frequency)
  Power dissipation
  Energy to perform a function

## Slide 14: Cost of Integrated Circuits
NRE (non-recurrent engineering) costs
  design time and effort, mask generation
  one-time cost factor
Recurrent costs
  silicon processing, packaging, test
  proportional to volume
  proportional to chip area

## Slide 15: Die Cost
Single die
Wafer
From http://www.amd.com
Going up to 17.7” (45 cm)

## Slide 16: Yield

## Slide 17: Reliability― Noise in Digital Integrated Circuits
i
(
t
)
Inductive coupling
Capacitive coupling
Power and ground
noise
v
(
t
)
V
DD

## Slide 18: DC Operation Voltage Transfer Characteristic
V(x)
V(y)
V
OH
V
OL
V
M
V
OH
V
OL
f
V(y)=V(x)
Switching Threshold
Nominal Voltage Levels
VOH = f(VOL)
VOL = f(VOH)
VM = f(VM)

## Slide 19: Mapping between analog and digital signals
V
IL
V
IH
V
in
Slope = -1
Slope = -1
V
OL
V
OH
V
out
“
0
”
V
OL
V
IL
V
IH
V
OH
Undefined
Region
“
1
”

## Slide 20: Definition of Noise Margins
Noise margin high
Noise margin low
V
IH
V
IL
Undefined Region
"1"
"0"
V
OH
V
OL
NM
H
NM
L
Gate Output
Gate Input

## Slide 21: Regenerative Property
Regenerative
Non-Regenerative

## Slide 22: Regenerative Property
A chain of inverters
v
0
v
1
v
2
v
3
v
4
v
5
v
6
Simulated response

## Slide 23: Fan-in and Fan-out
N
Fan-out N
Fan-in M
M

## Slide 24: The Ideal Gate
R
i
=
¥
R
o
= 0
Fanout = ¥
NMH = NML = VDD/2
g = 
V
in
V
out

## Slide 25: An Old-time Inverter
NM
H
V
in
(V)
V
out
(V)
NM
L
V
M
0.0
1.0
2.0
3.0
4.0
5.0
1.0
2.0
3.0
4.0
5.0

## Slide 26: Delay Definitions

## Slide 27: Ring Oscillator
T = 2
´
t
p
´
N

## Slide 28: A First-Order RC Network
v
out
v
in
C
R
tp = ln (2) t = 0.69 RC
Important model – matches delay of inverter

## Slide 29: Power Dissipation
Instantaneous power:
p(t) = v(t)i(t) = Vsupplyi(t)
Peak power:
Ppeak = Vsupplyipeak
Average power:

## Slide 30: Energy and Energy-Delay
Power-Delay Product (PDP) = E = Energy per operation = Pav  tp
Energy-Delay Product (EDP) = quality metric of gate = E  tp

## Slide 31: A First-Order RC Network
v
out
v
in
CL
R

## Slide 32: Summary
Digital integrated circuits have come a long way and still have quite some potential left for the coming decades
Some interesting challenges ahead
  Getting a clear perspective on the challenges and potential solutions is the purpose of this book
Understanding the design metrics that govern digital design is crucial
  Cost, reliability, speed, power and energy dissipation