## Slide 1: Digital Integrated Circuits A Design Perspective
Designing Combinational Logic Circuits
Jan M. Rabaey
Anantha Chandrakasan
Borivoje Nikolić
.

## Slide 2: Combinational vs. Sequential Logic
Combinational
Sequential
Output =
f
(
In
)
Output =
f
(
In, Previous In
)

## Slide 3: Static CMOS Circuit
At every point in time (except during the switching
transients) each gate output is connected to either
V
DD
or
V
ss
via a low-resistive path.
The outputs of the gates assume at all times the value
of the Boolean function, implemented by the circuit
(ignoring, once again, the transient effects during
switching periods).
This is in contrast to the
dynamic
circuit class, which
relies on temporary storage of signal values on the
capacitance of high impedance circuit nodes.

## Slide 4: Static Complementary CMOS
VDD
F(In1,In2,…InN)
In1
In2
InN
In1
In2
InN
PUN
PDN
PMOS only
NMOS only
PUN and PDN are dual logic networks
…
…
Notes: One and only one of the networks (PUN or PDN) is conducting in steady state

## Slide 5: NMOS Transistors in Series/Parallel Connection
    Transistors can be thought as a switch controlled by its gate signal
    NMOS switch closes when switch control input is high
X
Y
A
B
Y = X if A AND B
X
Y
A
B
Y = X if A OR B
NMOS Transistors pass a “strong” 0 but a “weak” 1

## Slide 6: PMOS Transistors in Series/Parallel Connection

## Slide 7: Complementary CMOS Logic Style

## Slide 8: Threshold Drops
VDD
VDD  0
PDN
0  VDD
CL
CL
PUN
VDD
0  VDD - VTn
CL
VDD
VDD
VDD  |VTp|
CL
S
D
S
D
VGS
S
S
D
D
VGS
Notes: Why PMOS in PUN and NMOS in PDN … threshold drop
NMOS transistors produce strong zeros; PMOS transistors generate strong ones

## Slide 9: Example Gate: NAND

## Slide 10: Example Gate: NOR

## Slide 11: Complex CMOS Gate
OUT = D + A • (B + C)
D
A
B
C
D
A
B
C
Notes: Shown synthesis of pull up from pull down structure

## Slide 12: Constructing a Complex Gate

## Slide 13: Stick Diagrams
C
A
B
X = C • (A + B)
B
A
C
i
j
j
VDD
X
X
i
GND
A
B
C
PUN
PDN
A
B
C
Logic Graph
Notes: Systematic approach to derive order of input signal wires so gate can be laid out to minimize area
Note PUN and PDN are duals (parallel <-> series)
Vertices are nodes (signals) of circuit, VDD, X, GND and edges are transitions

## Slide 14: Consistent Euler Path
j
VDD
X
X
i
GND
A
B
C
A
B
C
Notes: A path through all nodes in the graph such that each edge is visited once and only once.
The sequence of signals on the path is the signal ordering for the inputs.
PUN and PDN Euler paths are (must be) consistent (same sequence)
If you can define a Euler path then you can generate a layout with no diffusion breaks
A B C
C A B
B C A  no PDN
B A C
A C B -> no PDN
C B A

## Slide 15: OAI22 Logic Graph
C
A
B
X = (A+B)•(C+D)
B
A
D
VDD
X
X
GND
A
B
C
PUN
PDN
C
D
D
A
B
C
D

## Slide 16: CMOS Properties
Full rail-to-rail swing; high noise margins
Logic levels not dependent upon the relative device sizes; ratioless
Always a path to Vdd or Gnd in steady state; low output impedance
Extremely high input resistance; nearly zero steady-state input current
No direct path in steady state between power and ground; no static power dissipation
Propagation delay function of load capacitance and resistance of transistors

## Slide 17: Switch Delay Model
A
Req
A
Rp
A
Rp
A
Rn
CL
A
CL
B
Rn
A
Rp
B
Rp
A
Rn
Cint
B
Rp
A
Rp
A
Rn
B
Rn
CL
Cint
NAND2
INV
NOR2
Notes: Note capacitance on the internal node – due to the source grain of the two fets in series and the overlap gate capacitances of the two fets in series

## Slide 18: Input Pattern Effects on Delay
Delay is dependent on the pattern of inputs
Low to high transition
  both inputs go low
    delay is 0.69 Rp/2 CL
  one input goes low
    delay is 0.69 Rp CL
High to low transition
  both inputs go high
    delay is 0.69 2Rn CL
CL
B
Rn
A
Rp
B
Rp
A
Rn
Cint

## Slide 19: Delay Dependence on Input Patterns
A=B=10
A=1, B=10
A=1 0, B=1
time [ps]
Voltage [V]
Input Data Pattern | Delay (psec)
A=B=01 | 67
A=1, B=01 | 61
A= 01, B=1 | 64
A=B=10 | 45
A=1, B=10 | 80
A= 10, B=1 | 81
NMOS = 0.5m/0.25 m
PMOS = 0.75m/0.25 m
CL = 100 fF
Notes: Gate sizing should result in approximately equal worst case rise and fall times.
Reason for difference in the last two delays is due to internal node capacitance of the pulldown stack. When A transitions, the pullup only has to charge CL; when A=1 and B transitions pullup have to charge up both CL and Cint.
For high to low transitions (first three cases) delay depends on state of internal node. Worst case happens when internal node is charged up to VDD – VTn.
Conclusions: Estimates of delay can be fairly complex – have to consider internal node capacitances and the data patterns.

## Slide 20: Transistor Sizing
CL
B
Rn
A
Rp
B
Rp
A
Rn
Cint
B
Rp
A
Rp
A
Rn
B
Rn
CL
Cint
2
2
2
2
1
1
4
4
Notes: Assumes Rp = Rn

## Slide 21: Transistor Sizing a Complex CMOS Gate
OUT = D + A • (B + C)
D
A
B
C
D
A
B
C
1
2
2
2
4
4
8
8
6
3
6
6
Notes: For class lecture.
Red sizing assuming Rp = Rn
Follow short path first; note PMOS for C and B 4 rather than 3 – average in pull-up chain of three – (4+4+2)/3 = 3
Also note structure of pull-up and pull-down to minimize diffusion cap at output (e.g., single PMOS drain connected to output)
Green for symmetric response and for performance (where Rn = 3 Rp)
Sizing rules of thumb
PMOS = 3 * NMOS
1 in series = 1
2 in series = 2
3 in series = 3
etc.

## Slide 22: Fan-In Considerations
D
C
B
A
D
C
B
A
CL
C3
C2
C1
Distributed RC model
(Elmore delay)
tpHL = 0.69 Reqn(C1+2C2+3C3+4CL)
Propagation delay deteriorates rapidly as a function of fan-in – quadratically in the worst case.
Notes: While output capacitance makes full swing transition (from VDD to 0), internal nodes only transition from VDD-VTn to GND
C1, C2, C3 on the order of 0.85 fF for W/L of 0.5/0.25 NMOS and 0.375/0.25 PMOS
CL of 3.2 fF with no output load (all diffusion capacitance – intrinsic capacitance of the gate itself).
To give a 80.3 psec tpHL (simulated as 86 psec)

## Slide 23: tp as a Function of Fan-In
tpLH
tp (psec)
fan-in
Gates with a fan-in greater than 4 should be avoided.
tpHL
quadratic
linear
tp
Notes: Fixed fan-out (NMOS 0.5 micrcon, PMOS 1.5 micron)
tpLH increases linearly due to the linearly increasing value of the diffusion capacitance
tpHL increase quadratically due to the simultaneous incrase in pull-down resistance and internal capacitance

## Slide 24: tp as a Function of Fan-In and Fan-Out
Fan-in: quadratic due to increasing resistance and capacitance
Fan-out: each additional fan-out gate adds two gate capacitances to CL
tp = a1FI + a2FI2 + a3FO
Notes: a1 term is for parallel chain, a2 term is for serial chain, a3 is fan-out

## Slide 25: Fast Complex Gates: Design Technique 1
Transistor sizing
  as long as fan-out capacitance dominates
Progressive sizing
InN
CL
C3
C2
C1
In1
In2
In3
M1
M2
M3
MN
Distributed RC line
M1 > M2 > M3 > … > MN
(the fet closest to the
output is the smallest)
Can reduce delay by more than 20%; decreasing gains as technology shrinks
Notes: M1 have to carry the discharge current from M2, M3, … MN and CL so make it the largest
MN only has to discharge the current from MN (no internal capacitances)

## Slide 26: Fast Complex Gates: Design Technique 2
Transistor ordering
C2
C1
In1
In2
In3
M1
M2
M3
CL
C2
C1
In3
In2
In1
M1
M2
M3
CL
critical path
critical path
charged
1
01
charged
charged
1
delay determined by time to discharge CL, C1 and C2
delay determined by time to discharge CL
1
1
01
charged
discharged
discharged
Notes: For lecture.
Critical input is latest arriving signal
Place latest arriving signal (critical path) closest to the output

## Slide 27: Fast Complex Gates: Design Technique 3
Alternative logic structures
F = ABCDEFGH
Notes: Reduced fan-in -> deeper logic depth
Reduction in fan-in offsets, by far, the extra delay incurred by the NOR gate (second configuration).
Only simulation will tell which of the last two configurations is faster, lower power

## Slide 28: Fast Complex Gates: Design Technique 4
Isolating fan-in from fan-out using buffer insertion
CL
CL
Notes: Reduce CL on large fan-in gates, especially for large CL, and size the inverters progressively to handle the CL more effectively

## Slide 29: Ratioed Logic

## Slide 30: Ratioed Logic

## Slide 31: Ratioed Logic
V
DD
V
SS
PDN
In
1
In
2
In
3
F
R
L
Load
Resistive
N transistors + Load
• V
OH
= V
DD
• V
OL
=
R
PN
R
PN
+ R
L
• Assymetrical response
• Static power consumption
•
• t
pL
= 0.69 R
L
C
L
VDD

## Slide 32: Active Loads

## Slide 33: Pseudo-NMOS

## Slide 34: Pseudo-NMOS VTC
0.0
0.5
1.0
1.5
2.0
2.5
0.0
0.5
1.0
1.5
2.0
2.5
3.0
V
in
[V]
V
o
u
t
[V]
W/L
p
= 4
W/L
p
= 2
W/L
p
= 1
W/L
p
= 0.25
W/L
p
= 0.5

## Slide 35: Improved Loads

## Slide 36: Improved Loads (2)
V
DD
V
SS
PDN1
Out
V
DD
V
SS
PDN2
Out
A
A
B
B
M1
M2
Differential Cascode Voltage Switch Logic (DCVSL)

## Slide 37: DCVSL Example

## Slide 38: DCVSL Transient Response
0
0.2
0.4
0.6
0.8
1.0
-0.5
0.5
1.5
2.5
Time [ns]
V
o
l
t
a
g
e
[V]
A B
A B
A,B
A
,
B

## Slide 39: Pass-Transistor Logic

## Slide 40: Pass-Transistor Logic

## Slide 41: Example: AND Gate

## Slide 42: NMOS-Only Logic
0
0.5
1
1.5
2
0.0
1.0
2.0
3.0
Time [ns]
V
o
l
t
a
g
e
[V]
x
Out
In

## Slide 43: NMOS-only Switch
A =
2.5 V
B
C =
2.5
V
C
L
A =
2.5 V
C =
2.5 V
B
M
2
M
1
M
n
Threshold voltage loss causes
static power consumption
V
B
does not pull up to 2.5V, but 2.5V -
V
TN

## Slide 44: NMOS Only Logic: Level Restoring Transistor
M
2
M
1
M
n
M
r
Out
A
B
V
DD
V
DD
Level Restorer
X
• Advantage: Full Swing
• Restorer adds capacitance, takes away pull down current at X
• Ratio problem

## Slide 45: Restorer Sizing
0
100
200
300
400
500
0.0
1.0
2.0
W
/
L
r
=1.0/0.25
W
/
L
r
=1.25/0.25
W
/
L
r
=1.50/0.25
W
/
L
r
=1.75/0.25
V
o
l
t
a
g
e
[V]
Time [ps]
3.0
Upper limit on restorer size
Pass-transistor pull-down can have several transistors in stack

## Slide 46: Solution 2: Single Transistor Pass Gate with VT=0
Out
V
DD
V
DD
2.5V
V
DD
0V
2.5V
0V
WATCH OUT FOR LEAKAGE CURRENTS

## Slide 47: Complementary Pass Transistor Logic

## Slide 48: Solution 3: Transmission Gate
A
B
C
C
A
B
C
C
B
C
L
C
= 0 V
A =
2.5 V
C =
2.5 V

## Slide 49: Resistance of Transmission Gate

## Slide 50: Pass-Transistor Based Multiplexer
GND
VDD
In1
In2
S
S
S
S

## Slide 51: Transmission Gate XOR
A
B
F
B
A
B
B
M1
M2
M3/M4

## Slide 52: Transmission Gate Full Adder
Similar delays for sum and carry

## Slide 53: Dynamic Logic

## Slide 54: Dynamic CMOS
In static circuits at every point in time (except when switching) the output is connected to either GND or VDD via a low resistance path.
  fan-in of n requires 2n (n N-type + n P-type) devices
Dynamic circuits rely on the temporary storage of signal values on the capacitance of high impedance nodes.
  requires on n + 2 (n+1 N-type + 1 P-type) transistors

## Slide 55: Dynamic Gate
In1
In2
PDN
In3
Me
Mp
Clk
Clk
Out
CL
Out
Clk
Clk
A
B
C
Mp
Me
Two phase operation
Precharge (CLK = 0)
Evaluate (CLK = 1)
Notes: For class handout

## Slide 56: Dynamic Gate
In1
In2
PDN
In3
Me
Mp
Clk
Clk
Out
CL
Out
Clk
Clk
A
B
C
Mp
Me
Two phase operation
Precharge (Clk = 0)
Evaluate (Clk = 1)
on
off
1
off
on
((AB)+C)
Notes: For lecture
Evaluate transistor, Me, eliminates static power consumption

## Slide 57: Conditions on Output
Once the output of a dynamic gate is discharged, it cannot be charged again until the next precharge operation.
Inputs to the gate can make at most one transition during evaluation.
Output can be in the high impedance state during and after evaluation (PDN off), state is stored on CL
Notes: This behavior is fundamentally different than the static counterpart that always has a low resistance path between the output and one of the power rails.

## Slide 58: Properties of Dynamic Gates
Logic function is implemented by the PDN only
  number of transistors is N + 2 (versus 2N for static complementary CMOS)
Full swing outputs (VOL = GND and VOH = VDD)
Non-ratioed - sizing of the devices does not affect the logic levels
Faster switching speeds
  reduced load capacitance due to lower input capacitance (Cin)
  reduced load capacitance due to smaller output loading (Cout)
  no Isc, so all the current provided by PDN goes into discharging CL
Notes: CL being lower also contributes to power savings

## Slide 59: Properties of Dynamic Gates
Overall power dissipation usually higher than static CMOS
  no static current path ever exists between VDD and GND (including Psc)
  no glitching
  higher transition probabilities
  extra load on Clk
PDN starts to work as soon as the input signals exceed VTn, so VM, VIH and VIL equal to VTn
  low noise margin (NML)
Needs a precharge/evaluate clock

## Slide 60: Issues in Dynamic Design 1: Charge Leakage
CL
Clk
Clk
Out
A
Mp
Me
Leakage sources
CLK
VOut
Precharge
Evaluate
Dominant component is subthreshold current
Notes: leakage sources are reverse-biased diode and the sub-threshold leakage of the NMOS pulldown device.
Charge stored on CL will leak away with time (input in low state during evaluation)
Requires a minimum clock rate - so not good for low performance products such as watches (or when have conditional clocks)
PMOS precharge device also contributes some leakage due to reverse bias diode and subthreshold conduction that, to some extent, offsets the leakage due to the pull down paths.

## Slide 61: Solution to Charge Leakage
CL
Clk
Clk
Me
Mp
A
B
Out
Mkp
Same approach as level restorer for pass-transistor logic
Keeper
Notes: During precharge, Out is VDD and inverter out is GND, so keeper is on
During evaluation if PDN is off, the keeper compensates for drained charge due to leakage.
If PDN is on, there is a fight between the PDN and the PUN - circuit is ratioed so PDN wins, eventually
Note Psc during switching period when PDN and keeper are both on simultaneously

## Slide 62: Cascading Dynamic Gates
Clk
Clk
Out1
In
Mp
Me
Mp
Me
Clk
Clk
Out2
V
t
Clk
In
Out1
Out2
V
VTn
Only 0  1 transitions allowed at inputs!
Notes: Out2 should remain at VDD since Out1 transitions to 0 during evaluation. However, since there is a finite propagation delay for the input to discharge Out1 to GND, the second output also starts to discharge.
The second dynamic inverter turns off (PDN) when Out1 reaches VTn.
Setting all inputs of the second gate to 0 during precharge will fix it.
Correct operation is guaranteed (ignoring charge redistribution and leakage) as long as the inputs can only make a single 0 -> 1 transition during the evaluation period

## Slide 63: Domino Logic
In1
In2
PDN
In3
Me
Mp
Clk
Clk
Out1
In4
PDN
In5
Me
Mp
Clk
Clk
Out2
Mkp
1  1
1  0
0  0
0  1
Notes: Ensures all inputs to the Domino gate are set to 0 at the end of the precharge period. Hence, the only possible transition during evaluation is 0 -> 1

## Slide 64: Why Domino?
Clk
Clk
Ini
PDN
Inj
Ini
Inj
PDN
Ini
PDN
Inj
Ini
PDN
Inj
Like falling dominos!

## Slide 65: Properties of Domino Logic
Only non-inverting logic can be implemented
Very high speed
  static inverter can be skewed, only L-H transition
  Input capacitance reduced – smaller logical effort
Notes: First 32 bit micro (BellMAC 32) was designed in Domino logic
Now a rather rare design style due to non-inverting logic only

## Slide 66: Differential (Dual Rail) Domino
A
B
Me
Mp
Clk
Clk
Out = AB
!A
!B
Mkp
Clk
Out = AB
Mkp
Mp
Solves the problem of non-inverting logic
1 0
1 0
on
off
Notes: AND/NAND differential logic gate. The inputs and their complements come from other differential DR gates and thus all inputs are low during precharge and make a conditional transition from 0 to 1.
Annotations show state during evaluate cycle (CLK = 1)
Expensive - but can implement any arbitrary function.
Use significant power since they have a guaranteed transition every single clock cycle (regardless of signal statistics, since either Out or !Out will transition from 0 to 1).
Not ratioed (even though have a cross-coupled PMOS pair)

## Slide 67: np-CMOS
In1
In2
PDN
In3
Me
Mp
Clk
Clk
Out1
In4
PUN
In5
Me
Mp
Clk
Clk
Out2
(to PDN)
1  1
1  0
0  0
0  1
Only 0  1 transitions allowed at inputs of PDN Only 1  0 transitions allowed at inputs of PUN
Notes: Also called zipper logic - In4 and In5 must be from PDN’s
DEC alpha uses np-CMOS logic (Dobberpuhl)
Have to size the PUN’s to equalize the delay to that of the PDN’s
Really dense layouts and very high speed (20% faster than domino with the correct sizing)
Reduced noise margin (as with any dynamic gate)
Have two clock signals to generate and route - CLK and !CLK

## Slide 68: NORA Logic
In1
In2
PDN
In3
Me
Mp
Clk
Clk
Out1
In4
PUN
In5
Me
Mp
Clk
Clk
Out2
(to PDN)
1  1
1  0
0  0
0  1
to other
PDN’s
to other
PUN’s
WARNING: Very sensitive to noise!
Notes: NORA - no race CMOS